## Slide 1: Radio Astronomy Made Easy: Build DIY Radio Telescopes and Observe with an Intuitive GUI
Shin’ichiro Asayama (SKAO)
7 September 2025

## Slide 2: Radio Astronomy with commercially available equipment

## Slide 3: Radio Astronomy with commercially available equipment
Recent advancements in Information and communications technology (ICT) have enabled us to enjoy Radio Astronomy with commercially available equipment.
3

## Slide 4: Pulsar Detection Capability at SKAO HQ with Handmade instrument
The brightest pulsar visible in the northern hemisphere (PSR B0329+54) was detected with both the handmade loop feed installed on the mesh dish and the handmade 3D corner reflector.
Handmade 3D corer reflector results
Handmade loop Feed
See the recording of Shriram’s talk: https://confluence.skatelescope.org/display/SKAQA/SKAO+Speaker+Series
Shriram Vijaysampath
Student: Physics with Astrophysics at the University of Warwick

## Slide 5: Deployment of 6ft Deep dish(f/D~0.25) @610 MHz by a High school Student
Measured FWHM ~ 23 deg @610MHz
Dipole
Rod
reflector
The brightest pulsar visible in the northern hemisphere (B0329+54) was detected at 610MHz.
15-day integrated pulse in July 2025
DM=0
DM=26.7641
DM=54
A hacksaw is all you need!

## Slide 6: W3(OH)12.2 GHz Methanol Maser Detection with a 1m satellite Dish
W3(OH) 10 days of observations
Set the dish at the declination of W3(OH) and let the target drift through the beam daily – Patience is needed!!
A cheap Low-Noise Block (LNB) (< £10 )
Satellite TV receiver to provide DC power and a 22kHz tone for the LNB to activate “high band” (LO=10.6GHz).
The LNB LO offset was checked with Astra 3B satellite beacon at 11446.7266 MHz.
Data was recorded with Airspy mini SDR (BW = 6MHz).
Daily VLSR correction was done using Astropy.
Reference:
Project EM01: Mini maser telescope: detecting 12.2 GHz methanol masers with a 1-metre dish http://parac.eu/projectem01.htm
Satellite TV receiver
2 Way Satellite
Cable Splitter
DC+
22kHz
tone
Airspy
mini
IF=1.58GHz

## Slide 7: 6ft Dish (F/D~0.25) Assembly, Integration, Verification and Commissioning (AIVC)
LNB (Low-Noise Block) Modification
An open-ended circular waveguide with a diameter just above the cutoff dimension is well-suited for a very deep dish (F/D ~ 0.25).
Science Verification and Commissioning
Assembly, Integration and Validation (AIV)
Satellite TV receiver to provide DC power and a 22kHz tone for the LNB to activate “high band” (LO=10.6GHz).
The LNB LO offset was checked with Astra 3B satellite beacon at 11446.7266 MHz.
Optimisation of focus and determination of beam offsets using the Sun.
W3(OH)12.2 GHz Methanol Maser Detection
Set the dish at the declination of W3(OH) and let the target drift through the beam daily.
~10 min
ON/OFF
2-days
~10 min
Frequency
Switch
10-days
A hacksaw is all you need!

## Slide 8: Detection of Hydrogen 21cm emission line using inexpensive/commercially available equipment

## Slide 9: Detection of Hydrogen 21cm emission line using inexpensive/commercially available equipment
Freq = | 1.42 | GHz
Waveguide Diameter = | 15.8 | cm
TE11 Cutoff = | 27.0 | cm
TM01 Cutoff = | 20.7 | cm
Probe placement = | 8.5 | cm
Feedhorn Length = | 25.5 | cm
http://www.setileague.org/hardware/feedchok.htm
9

## Slide 10: High School Student Riku’s Camping Mat horn antenna
Cantenna
SAWbird+ H1
Amp
SDR
10
Horn
Antenna

## Slide 11: Time-lapse
Need good operators (Cats!)

## Slide 12: Exploring Galactic Rotation Curve with a 2.5-ft Telescope: A Work Experience Project
Telescope positioning was with iPhone's Compass and Level (~5 accuracy). Although rough pointing directions, the measured hydrogen line profiles reasonably agree with the professional hydrogen line profiles.
Lovell Telescope
250ft
(76.2 m)
2.5ft
(76.2cm)
150km/s
With rough velocity determination by eye, the rotation curve of the galaxy were derived using the tangent point method. The flat Galactic rotation curve can be seen. This suggests that the mass distribution of the Galaxy is not uniform, and that there is some unseen matter that affects the orbital speeds of stars and gas.
The expected profiles (Orange dashed lines) downloaded from:
Argelander-Institut furAstronomie (University of Bonn)
125km/s
100km/s
75km/s
50km/s

## Slide 13: Workshop building SKAO Table-top Radio Telescopes (TTRT)
Students in Görlitz 🇩🇪 built tabletop radio telescopes with DZA and observed the Milky Way.

## Slide 14: SKAO TTRT Outreach Highlights at IAU GA in Cape Town
SKAO’s TTRT captivated audiences at the International Astronomical Union General Assembly (IAU GA) with hands-on demos and educational sessions.
The outreach extended to three Cape Town universities, Stellenbosch, and University of Western Cape.
A further session was staged for younger children at the Cape Town Science Centre.

## Slide 15: A totally nutty radio telescope—because why not?

## Slide 16: Science influencer Big Manny’s Balloon Horn Antenna
16

## Slide 17: Cat Tunnel Radio Telescope
Horn antenna
(Template)
Cat tunnel
Pop the cat tunnel over the horn,
bend the wire to shape it,
and snip off any extra fabric to make it fit!
17

## Slide 18
Bird Feeder Radio Telescope

## Slide 19: Portable Mini Umbrella Hat Radio Telescope
2. Make a loop feed with the tin lid
Enjoy Cookies
3. Glue tin foil over the Umbrella Hat
4. Fix the loop feed on the umbrella hat with the headband.
19

## Slide 20: BBQ Grill Net Radio Telescope
Plastic
Cable
Ties
SMA
Connector
Brass Round
Tube 3mm
BBQ Grill Mesh ~30cm
~12.5cm
~12.5cm
Monopole ~ 15.5cm
Dia. ~3mm
SMA Connector is
attached with cable ties
Brass Round
Tube
BBQ Nets are assembled with cable ties
SDR
DC5V
from USB
SAWbird+ H1 +
Amp
20

## Slide 21: Paper Craft Radio Telescope
Print the template at 100% or actual size on A3 paper. Do not scale.
Make a circular column by rolling the template and tape or glue it.
Twist tin foil into a string, wrap it around the guide, and secure it with tape to create a helical antenna
Use a circular board larger than 20 cm (such as candy lids) and 500 ml plastic bottles
Wrap cardboard around the plastic bottle to adjust the column's thickness.
Attach the helical antenna to the column built in step 7.
Connect the centre pin of the SMA connector to the helical antenna using tin foil and secure it with tape. Use a tester to check the electrical connectivity between the top of the helical antenna and the centre sleeve of the SMA connector
Use metal washers for electrical connections.
Centre pin of the SMA connecter
Attach an SMA connector to the lid using screws, washers, and nuts.
Use a tester, such as a multimeter, to check the electrical connectivity between the ground plane and the SMA connector.
Glue tin foil to the lid as a ground plane, drill a hole in the centre of the lid for the bottle opening and attach the bottle to the lid using the plastic bottle cap.
SMA
connector
Bottle
Cap
21

## Slide 22: SKAO TTRT Windows App Demo
https://gitlab.com/ska-telescope/ska-tabletop-radiotelescope/-/packages/40199961

## Slide 23: HI Observation Software for Windows
Setting up an observation environment posed a significant barrier for general users.
To facilitate HI observations, SKAO has developed a dedicated application for Windows PCs.
Thanks to this new application, the number of successful observations has increased markedly.

## Slide 24: SKAO Windows App Demo
24
RF
Termination

## Slide 25: SKAO Windows App Demo
25

## Slide 26: Thank you!

## Slide 27: The 21 cm Spectral Line of Neutral Hydrogen
Because of the motion of the emitting atoms relative to the observer the hydrogen line does not appear at a single frequency but is spread out and shifted from its “rest” frequency of 1420.406 MHz. The spread is due to random motions within a cloud of gas and the shift is due to the overall or “bulk” motion of the cloud itself. The non-relativistic Doppler shift formula:
if 𝒇𝒐𝒃𝒔 is below 𝒇𝒆𝒎 the gas is moving away from the observer (receding) and the radial velocity is said to be positive
if 𝒇𝒐𝒃𝒔 is above 𝒇𝒆𝒎 the gas is moving towards the observer (approaching) and the radial velocity is said to be negative
27

## Slide 28: Japanese Earth-Moon-Earth (EME) Communication Antenna
The diurnal and annual doppler shift of the period on B0329+54 due to the daily rotation of the Earth and its annual orbit around the sun.
DM Check
Period Check

## Slide 29: Kitchenware Radio Telescope Characteristics
The kitchenware radio telescope is a 3D corner reflector with a 30 cm (~1.5l) on each edge.
The 3D corner reflector antenna was modelled in the OpenMOM.
A matching circuit for a 3D reflector antenna is often needed, but the antenna can match 50ohm at a specific frequency. This can be seen in measuring the real antenna's return loss by finding the optimal point of the position of the monopole.
The calculated gain of the 30cm 3D corner reflector is about 14.8 dBi.
Reference
http://on5au.be/content/a10/vhf/3c.html
https://blog.freifunk-mainz.de/wp-content/uploads/2013/08/Shortened-3D-Corner-Reflector-Antenna.pdf
http://emoss.starfree.jp/OpenMOM/index.html
OpenMoM Model
30cm
30cm
30cm
~12.5cm
~12.5cm
Monopole ~ 16cm
Dia. ~2mm